## Slide 1: ARP Packet Format
Destination address
Source address
Type
0x8060
ARP or RARP
Padding
CRC
Hardware type (2bytes)
Protocol type (2 bytes)
Operation code (2 bytes)
Hardware address length (1byte)
Protocol address length (1 byte)
Source hardware address
6
6
2
28
10
Ethernet header
Source protocal address
Target protocal address
Target hardware address
4

## Slide 2: ARP Flow
192.168.0.100
11:11:11:11:11:11
192.168.0.200
22:22:22:22:22:22
ARP Request (Broadcast)
ARP Reply (Unicast)
Source hardware address – 11:11:11:11:11:11
Source protocol address – 192.168.0.100
Destination hardware address – 00:00:00:00:00:00
Destination protocol address – 192.168.0.200
Source hardware address – 22:22:22:22:22:22
Source protocol address – 192.168.0.200
Destination hardware address – 11:11:11:11:11:11
Destination protocol address –192.168.0.100