## Slide 1: CUDA Container OCI Runtime Spec
# docker run --gpu all nvidia/cuda:9.0-base nvida nvidia-smi
"hooks": {
"prestart": [
{
"path": “/usr/bin/nvidia-container-runtime-hook”,
"args": ["nvidia-container-runtime-hook ", “prestart"],
"env": [“CUDA_VERSION=9.0.176”, “CUDA_PKG_VERSION=9-0=9.0.176-1”,
“NVIDIA_VISIBLE_DEVICES=all“, “NVIDIA_DRIVER_CAPABILITIES=“compute,utility”,
"NVIDIA_REQUIRE_CUDA=cuda>=9.0“, "LD_LIBRARY_PATH=/usr/local/nvidia/lib:/usr/local/nvidia/lib64“
]
},
],
}
OCI Runtime Spec

## Slide 2: CUDA Container Init
nvidia-container-cli CLI
libnvidia-container
nvidia-container-runtime-hook CLI
Hook Config File
runc CLI
Prestart Hook
STDIN : Container Status
(Init PID, Rootfs Path)
ENV : GPU, CUDA Config
(GPU Device, CUDA Version)
Exec with Container,
GPU, CUDA Arguments
Container
(Namespace, Rootfs)
Create Namespace,
Set rootfs (clone())
2
3
4
Exec App
5
1

## Slide 3: CUDA Container Stack
Host Hardware
Host Kernel
/dev/nvidia0
/dev/nvdia1
/dev/nvdia2
/dev/nvdia3
NVIDIA
GPU 0
NVIDIA
GPU 1
NVIDIA
GPU 2
NVIDIA
GPU 3
NVIDIA CUDA Device Driver
Container A
/dev/nvidia0
/dev/nvidia1
NVIDIA CUDA Lib/Toolkit
Container B
/dev/nvdia0
/dev/nvdia2
NVIDIA CUDA Lib/Toolkit
/dev/nvdia3
Container C
/dev/nvdia3
NVIDIA CUDA Lib/Toolkit
Bind Mount